## Slide 1: SMART LIGHT CONTROL
Components Needed:
Arduino Board: e.g., Arduino Uno
LED: Preferably RGB for colour variations
Resistor: To limit current through the LED
Relay Module: If controlling high-voltage lights
Breadboard and Jumper Wires: For connections
Wi-Fi Module: e.g., ESP8266 or ESP32 for communication over Wi-Fi

## Slide 2
Steps to Build the System:
1. Hardware Setup:
Connect the LED to the Arduino board using a resistor to limit the current.
If using a relay module, connect it in parallel with the light source controlled by one of the GPIO pins on the Arduino board.
Connect the Wi-Fi module to the Arduino board to enable communication over Wi-Fi.

## Slide 3
2. Arduino Firmware:
Program the Arduino using C/C++ within the Arduino IDE.
Use libraries like ESP8266WiFi or WiFi.h to establish communication via Wi-Fi.
Write code to listen for incoming commands (e.g., turn on/off, change colors) sent from the mobile app.
On receiving data, check what action needs to be taken and control the LED accordingly.

## Slide 4
3. Mobile App Development:
Develop a mobile app using frameworks like React Native or Flutter.
Provide users with buttons/sliders to turn lights on/off and adjust brightness or colors.
Use HTTP requests over REST API calls to send commands to the Arduino board.
4. Integration:
Ensure the mobile app can connect to the Arduino board over the local network or Wi-Fi.
Test the system to ensure the LED responds to app-based commands